## Slide 1: Lecture 6 – IP Subnetting and IPv6 Addressing
COMP1002 (Cybersecurity and Networks)

## Slide 2: Overview
Explain the need for subnetting (ch 11)
Calculate addressing for given network and subnet mask
Describe Variable Length Subnet Masking (VLSM)
Design and implement hierarchical addressing
IPv6 addressing (ch 12)
IPv6 business network deployment

## Slide 3: Part 1: IP Subnetting

## Slide 4: Why subnetting
To provide levels of hierarchy
  Flat networking is difficult to manage
E.g. – UoP network – 141.163.0.0/255.255.0.0
  All broadcasts would propagate to whole network
  Connectivity – stacks of interconnected switches
  Implementation: combination of
    255.255.255.0 – typical network segments
    255.255.255.240, 255.255.255.252 – core routers
Replicate division of location/roles/device types
Communication between subnets requires a router
No difference between network and subnet
Notes: Switches propagate broadcasts out all interfaces except the interface on which it was received. Only routers do not propagate broadcasts (or routers segment broadcast domains).
Device types: e.g., all hosts, all servers, all printers.
Roles: e.g., students, HR, staff

## Slide 5: Subnetting
Creating multiple networks from a single address block
  Method “borrow” network bits from the host part
  /m network, borrowing n bits
    2^n subnets
    2^(32-n-m) hosts/subnet

## Slide 6: Subnetting examples

## Slide 7: Subnetting examples
Borrow 1 bit – 2 networks

## Slide 8: Subnetting examples
Borrow 2 bits –4 subnets, 62 hosts/subnet

## Slide 9: Subnetting examples – subnet a /16 network

## Slide 10: Subnetting examples – subnet a /16 network

## Slide 11: Subnetting examples
Borrow 7 bits – 128 networks

## Slide 12: Subnetting in action

## Slide 13: Finding the right solution
Determine the number of networks
Determine the number of hosts/network
Do the maths!

## Slide 14: Finding the right solution
A.B.C.D/m network, borrow n bits
  2^n subnets
  2^(32-m-n) addresses/subnet
  (2^(32-m-n) – 2) usable hosts
141.163.0.0/16, borrow 7 bits
  m=16, n=7
  2^7 = 128 subnets
  2^(32-7-16) = 2^9 = 512 addresses/subnet
  2^(32-7-16) = 2^9-2 = 510 hosts/subnet

## Slide 15: Variable Length Subnet Masking
Why? To reduce wastage

## Slide 16: VLSM

## Slide 17: VLSM - implementation

## Slide 18: (sub)subnetting

## Slide 19: Subnetting Example
Class C address is granted, e.g., 192.168.1.0 (with a total of 256 IP addresses allocatable).
Requirements:
  3 networks with 60 hosts
  2 networks with 20 hosts
Subnetting
  If borrow 2 bits, it will have 4 subnets, each with 2^(6) – 2 = 64 – 2 = 62 hosts
  If borrow 3 bits, it will have 8 subnets, each with 2^(5) – 2 = 32 – 2 = 30 hosts
  First borrow 2 bits, to have 4 subnets, A, B, C D, each can have 62 hosts. Then from subnet D, further borrow 1 bit, to have two further subnets, each having 30 hosts (e.g. D1, D2).
  Can you work out host IP address range, network address and netmask for each subnet (A, B, C, D1 and D2)?
A
B
C
D1
D2
Notes: Netmask for A/B/C: 255.255.255.192
Netmask for D1/D2: 255.255.255.224
Network address for A: 192.168.1.0
Network address for B: 192.168.1.64
Network address for C: 192.168.1.128
Network address for D1: 192.168.1.192
Network address for D2: 192.168.1.224

## Slide 20: VLSM

## Slide 21: VLSM
PerthHQ - 26
SydneyHQ - 10

## Slide 22: IPv4 address planning and assignment
Aims
  Preventing Duplication of Addresses
  Providing and Controlling Access
  Monitoring Security and Performance
Categories of hosts
  End user clients - DHCP
  Servers and peripherals - static
  Hosts accessible from the Internet – static, public
  Intermediary devices – static, predictable
  Gateway – static, first or last
Notes: Intermediary devices – these devices are assigned addresses for network management, monitoring, and security.

## Slide 23: Activities and labs
11.9.3 – VLSM design and implementation practice
11.10.1 – Design and Implement VLSM addressing scheme
11.8.6 – VLSM practice

## Slide 24: Part 2: IPv6

## Slide 25: IPv4 is running out
Source: cisco

## Slide 26: IPv6
Why?
  Because IPv4 ran out
What
  More addresses
    128 bits
    No more NAT
  Smaller header
  Better security
    Natively integrated in header functionality

## Slide 27: IPv6 – IPv4 coexistence

## Slide 28: IPv4 vs IPv6

## Slide 29: IPv4 vs IPv6

## Slide 30: IPv6
Version - 4-bit, set to 0110.
Traffic Class - 8-bit
  Equivalent to the IPv4 Differentiated Services (DS) field
  6-bit Differentiated Services Code Point (DSCP) - classify packets
  2-bit Explicit Congestion Notification (ECN) - traffic congestion control.
Flow Label - 20-bit field for real-time applications
  Inform switches and routers to maintain same path for flow
Payload Length - 16-bit, equivalent to IPv4 Total Length
  Entire packet (fragment) size, including header and optional extensions.
Next Header - 8-bit field is equivalent to the IPv4 Protocol field.
Hop Limit - 8-bit field replaces the IPv4 TTL field.
Source Address - 128-bit - IPv6 address of sending host.
Destination Address - 128-bit field - IPv6 address of receiving host.

## Slide 31: IPv6 representation – hex notation

## Slide 32: IPv6 representation – hextets

## Slide 33: IPv6 representation – omitting 0s
Leading 0s in hextets can be omitted
  NOT trailing 0s !
All-zero hextets can be replaced by double colon
  Only once in an address

## Slide 34: IPv6 communication
Unicast – identify an IPv6 interface
Multicast – send IPv6 packets to multiple destination
Anycast – unicast address that can be assigned to multiple devices
  Packet routed to nearest such device
No broadcast address
  Replaced by an IPv6 all-nodes multicast (same)

## Slide 35: IPv6 networks
Typical prefix - /64

## Slide 36: IPv6 addresses
Global unicast – same as IPv4 public – not strictly required
Link-local – for link communication – every IPv6 host is required to have one, automatically created
  FE80::/10
  Not routable
Unique local – similar to RFC1918 IPv4
  FC00::/7 to FDFF::/7
  Not routable
Loopback
  All-zero except the last bit
  ::1
Unspecified – use as source when n IPv6 assigned
  All-zero
  ::

## Slide 37: IP link-local communication

## Slide 38: IPv6 global unicast addresses
Three parts
  Global routing prefix (aka network portion)
    assigned by ISP, typically /48
  Subnet ID
    Used by organisation to identify subnets
  Interface ID (aka host portion)

## Slide 39: IPv6 global unicast address – example

## Slide 40: IPv6 address - router configuration

## Slide 41: IPv6 address – host configuration

## Slide 42: EUI-64 – the process

## Slide 43: EUI-64 – the process
MAC address
  24bit OUI
  24bit device identifier
EUI-64 interface ID is made of three parts:
  24-bit OUI from the client MAC address, but the 7th bit (the Universally/Locally (U/L) bit) is reversed - if the 7th bit is a 0 it becomes a 1, and vice versa.
  The inserted 16-bit value FFFE (in hexadecimal)
  24-bit Device Identifier from the client MAC address

## Slide 44: EUI-64 – the result

## Slide 45: Static link-local addresses
Router(config-if)#ipv6 address link-local-address link-local

## Slide 46: Verify IPv6 configuration

## Slide 47: IPv6 subnetting
No need to save IP address space
  Wastage is irrelevant for 2128 addresses
Implemented for hierarchical reasons
  Same as other-than-wastage IPv4 reasons

## Slide 48: IPv6 subnetting - /48 block

## Slide 49: IPv6 subnetting example

## Slide 50: Labs
12.9.1 – Implement a subnetted IPv6 addressing scheme (optional)