## Slide 1: Lecture 8 - VLANs
COMP1002 (Cybersecurity and Networks)

## Slide 2: Overview
Virtual LANs (VLANs) (CCNA2/ch3)
  Definition, benefits, types, tagging
  Configuration
  Trunking concepts, issues, attacks
InterVLAN routing (CCNA2/ch4)
  Concept and configuration

## Slide 3: Virtual LANs (VLANs)

## Slide 4: Objectives
Purpose and benefits of VLANs
Functionality of VLANs
Configure
  VLAN port assignment
  Trunking
  Dynamic Trunking Protocol (DTP)
Troubleshoot VLAN and trunk configuration
Configure security features

## Slide 5: VLAN definition
A VLAN is a logical group of network stations and devices.
  Important feature of Ethernet switching
Aim of VLANs - provide logical grouping for different users regardless of their physical location.
  Each VLAN – separate logical network
  Packets for other VLANs must be forwarded through a routing device
  Each VLAN is a separate broadcasting domain
e.g. grouping different departments
  Marketing department users – Marketing VLAN
  Engineering department users – Engineering VLAN
  ...even though they may be in the same office.
Why?
  Access to resources
  Security
  Improved data flow

## Slide 6: Logical versus Physical Topology
Three broadcast domains using switches and VLANs.
Members of same VLAN may be remote to each other.
The VLAN server can be located in a server farm.
Result: increased overall network performance by logically grouping users and resources together.

## Slide 7: VLAN benefits
Security - Groups that have sensitive data are separated from the rest of the network, decreasing the chances of confidential information breaches.
Cost reduction - reduced need for upgrades, efficient use of bandwidth/uplinks.
Better performance - reduce unnecessary traffic on the network
Shrink broadcast domains - Dividing a network into VLANs reduces the number of devices in the broadcast domain.
Improved IT staff efficiency - easier to manage the network because users with similar network requirements share the same VLAN.
Simpler project and application management - VLANs aggregate users and network devices to support business or geographic requirements.

## Slide 8: VLAN types
Data
  User generated traffic
Voice
  For IP telephony
Default
  VLAN1
  All ports allocated to it by default
Native
  In relation to a trunk port
  Carries untagged traffic
Management
  Used to manage the switch (SVI)
  VLAN1 by default

## Slide 9: VLAN trunks
point-to-point link between two network devices that carries more than one VLAN

## Slide 10: Frame Tagging
Each frame on trunk is tagged to identify VLAN it belongs to.
Trunking that uses frame tagging achieves faster delivery of frames and makes management easier.
Frame tagging adopted as standard by IEEE.

## Slide 11: VLAN tag fields
Type - A 2-byte value called the tag protocol ID (TPID) value.
  Ethernet - 0x8100.
User priority - A 3-bit value that supports level or service implementation.
Canonical Format Identifier (CFI) - A 1-bit identifier that enables Token Ring frames to be carried across Ethernet links.
VLAN ID (VID) - A 12-bit VLAN identification
  up to 4096 VLAN IDs.
After the switch inserts the Type and tag control information fields, it recalculates the FCS values and inserts the new FCS into the frame.

## Slide 12: Voice VLAN tagging

## Slide 13: Quiz 1
In a switched network without VLAN, PC1 is sending a layer 2 broadcast, which of the following is correct?
(a). The broadcast frame will reach PC2 – PC6.
(b). The broadcast frame will only reach PC4.
(c). The broadcast frame will reach PC4, PC5 and PC6.
(d). None of the above is correct.
Go to www.menti.com and use the code 1915 1067

## Slide 14: Quiz 2
In a switched network with 3 VLANs configured (VLAN10, VLAN20 and VLAN30), PC1 sends an ARP broadcast frame. Which of the following is correct regarding PC(s) which will receive the ARP broadcast frame?
(a). PC4
(b). PC4 and PC6
(c). PC4, PC5 and PC6
(d). None of the above
Go to www.menti.com and use the code 1915 1067

## Slide 15: VLAN configuration

## Slide 16: Normal range VLANs
Normal range VLANs are numbered between 1 and 1005.
IDs of 1 and 1002-1005 are automated created.
Extended range VLANs are numbered 1,006 to 4,094.

## Slide 17: VLAN – assign a switch port

## Slide 18: Delete a VLAN

## Slide 19: Verify VLANs and membership

## Slide 20: Trunk configuration

## Slide 21: Resetting trunks

## Slide 22: Verify trunk configuration

## Slide 23: Dynamic Trunking Protocol (DTP)

## Slide 24: DTP modes

## Slide 25: DTP modes
switchport mode access - permanent nontrunking mode and negotiates to convert the link into a nontrunk link. The interface becomes a nontrunk interface, regardless of whether the neighboring interface is a trunk interface.
switchport mode dynamic auto - able to convert the link to a trunk link. The interface becomes a trunk interface if the neighboring interface is set to trunk or desirable mode. It is the default switchport mode.
switchport mode dynamic desirable - actively attempt to convert the link to a trunk link. Interface becomes trunk if neighboring interface is trunk, desirable, or auto. It is the default switchport mode on older switches(2950 and 3550).
switchport mode trunk - permanent trunking mode, negotiates to convert neighboring link into trunk. Interface becomes trunk even if the neighboring interface is not trunk.
switchport nonegotiate - Prevents the interface from generating DTP frames. Can use this command only when the interface switchport mode is access or trunk. You must manually configure the neighboring interface as a trunk interface to establish a trunk link.

## Slide 26: Troubleshoot VLANs
IP issues
  Misconfigured clients
Missing VLANs
  VLANs must be present on all transit switches and ports must be assigned to it
Misconfigured trunks/links
  Check interface and trunk settings - show interfaces trunk

## Slide 27: Trunk problems

## Slide 28: Switch attacks – switch spoofing
Notes: A VLAN hopping attack. The attacker configure the host to spoof 802.1Q signalling and DTP signalling to trunk with the connecting switch.

## Slide 29: Double tagging attack

## Slide 30: PVLAN edge
Notes: Private VLAN – protected ports

## Slide 31: Summary
VLAN segmentation
  Definitions
  Benefits
  Types
VLAN environment
  Trunks
  Tagging
  Implementation
  Troubleshooting
VLAN security
Notes: 31

## Slide 32: Activities and labs (CCNA2)
3.3.12 - VLAN configuration
3.6.1 - Implement VLANs and Trunking

## Slide 33: Inter-VLAN Routing

## Slide 34: Objectives
Inter-VLAN routing
  enable
  configure
  troubleshoot

## Slide 35: Inter-VLAN routing

## Slide 36: Legacy inter-VLAN routing

## Slide 37: Router-on-a-stick

## Slide 38: Switch-based inter-VLAN routing

## Slide 39: Configure legacy inter-VLAN routing

## Slide 40: Router-on-a-stick – switch configuration

## Slide 41: Router-on-a-stick – router configuration

## Slide 42: Layer 3 switches
Routed port - pure Layer 3 interface similar to a physical interface on a Cisco IOS router.
Switch virtual interface (SVI) - virtual VLAN interface for inter-VLAN routing.

## Slide 43: Switched architecture

## Slide 44: Inter-VLAN routing with routed ports

## Slide 45: Switch configuration issues
VLANs - defined across all the switches, enabled on the trunk ports.
Ports - must be in the right VLANs.
SVIs - correct IP address or subnet mask.
  SVI – up and match with the VLAN number.
Routing - enabled.
  Each interface or network should be added to the routing protocol.
Hosts - correct IP address or subnet mask, default gateway associated with SVI or routed port.

## Slide 46: Labs (CCNA2)
4.2.7 – Configure Router-on-a-stick interVLAN routing