## Slide 1: Lecture 9 – Routing Concepts and Static Routing
COMP1002 (Cybersecurity and Networks)

## Slide 2: Overview
Routing concepts (ch 14, CCNA2)
  Primary functions and features of a router
  Connecting devices for a small network
  Configure basic router settings using CLI
  Verify connectivity between networks
  Encapsulation/decapsulation
  Path determination function of a router
  Building a routing table
Static routing (ch 15, CCNA2)
  Advantages and disadvantages
  Configuration
  Classful and CIDR addressing
  Summary routes
  Floating static routes

## Slide 3: Functions of a router
To route!
  Determine the best path for a packet
  Forward the packet
A router connects one network to another network.
Communication between networks would not be possible without a router determining the best path to the destination and forwarding traffic to the next router along that path.
The router is responsible for the routing of traffic between networks.

## Slide 4: Routing process
Router examines the destination IP of each received packet and decides what to do with it based on a routing table
  Match found
    Directly connected to the network – send the packet to destination
    Not directly connected – forward it to another router
  No match found – drop the packet
Routing – layer 3 (based on IP addresses)
  Routers operate at layers 1,2, and 3

## Slide 5: Documenting network addressing

## Slide 6: Console access
Notes: ISR: integrated service router

## Slide 7: Configure interface

## Slide 8: Configure serial interface

## Slide 9: Configure ipv6 interface

## Slide 10: Configure loopback interface

## Slide 11: show/output filters
section - Shows entire section that starts with the filtering expression
include - Includes all output lines that match the filtering expression
exclude - Excludes all output lines that match the filtering expression
begin - Shows all the output lines from a certain point, starting with the line that matches the filtering expression
sh ip int bri | include up

## Slide 12: Send a packet – source PC to router

## Slide 13: Send a packet – router to router

## Slide 14: Send a packet – router to router

## Slide 15: Send a packet – router to destination

## Slide 16: Packet forwarding decision process

## Slide 17: Best path?
What is the best route from Plymouth to Heathrow?

## Slide 18: Best path?

## Slide 19: Load balancing

## Slide 20: Administrative distances
Define the preference of a routing source.
Each routing source - prioritized in order of most- to least-preferable using an administrative distance value.
Cisco routers use the AD feature to select the best path when it learns about the same destination network from two or more different routing sources.

## Slide 21: Administrative distances

## Slide 22: The routing table

## Slide 23: The routing table
Local Route interfaces - Added when an interface is configured and active. This entry is only displayed in IOS 15 or newer for IPv4 routes and all IOS releases for IPv6 routes.
Directly connected interfaces - Added to the routing table when an interface is configured and active.
Static routes - Added when a route is manually configured and the exit interface is active.
Dynamic routing protocol - Added when routing protocols that dynamically learn about the network, such as EIGRP or OSPF, are implemented and networks are identified.

## Slide 24: The routing table

## Slide 25: Routing entries

## Slide 26: Static routes

## Slide 27: Static routing
Not advertised over the network - better security.
Less bandwidth than dynamic routing protocols
No CPU cycles are used to calculate and communicate routes.
The path a static route uses to send data is known.
Initial configuration and maintenance is time-consuming.
Configuration is error-prone, especially in large networks.
Admin intervention - required to maintain changing route information.
[Maintenance] does not scale well with growing networks
Requires complete network knowledge of whole network for proper implementation.

## Slide 28: Static routes to/from stub networks

## Slide 29: When to use static routes
Connect to a specific network
Connect a stub router
Summarize routing table entries
Create a backup route
Types:
  Standard static route
  Default static route
  Summary static route
  Floating static route

## Slide 30: Standard static routes

## Slide 31: Default static routes
Set a default static route in R1 to point to R2 for all traffic going to Internet.

## Slide 32: Summary static routes
Multiple static routes can be summarized into a single static route if:
  Destination networks are contiguous and can be summarized into a single network address.
  Multiple static routes all use the same exit interface or next-hop IP address.

## Slide 33: Floating static routes
Backup route for a dynamic primary route
Higher AD

## Slide 34: Configure static routes

## Slide 35: Specifying next hop
Next-hop route - Only the next-hop IP address is specified.
Directly connected static route - Only the router exit interface is specified.
Fully specified static route - The next-hop IP address and exit interface are specified.

## Slide 36: Configure next-hop static routes

## Slide 37: Configure directly connected static routes

## Slide 38: Next-hop vs directly connected
Configuring a directly connected static route with an exit interface allows the routing table to resolve the exit interface in a single search, instead of two.
Although the routing table entry indicates “directly connected”, the AD of the route is still 1.
Only a directly connected interface can have an administrative distance of 0.
point-to-point interfaces - point to the exit interface or to the next-hop address.
multipoint/broadcast interfaces - point to a next-hop address.

## Slide 39: Fully specified static routes

## Slide 40: Verify static routes
ping and traceroute
show ip route
show ip route static
show ip route network

## Slide 41: Default static route syntax

## Slide 42: Configure a default static route

## Slide 43: Verify a default static route

## Slide 44: Next-hop options
The next hop can be identified by an IPv6 address, exit interface, or both. How the destination is specified creates one of three route types:
  Next-hop static IPv6 route - Only the next-hop IPv6 address is specified.
  Directly connected static IPv6 route - Only the router exit interface is specified.
  Fully specified static IPv6 route - The next-hop IPv6 address and exit interface are specified.

## Slide 45: IPv6 route command
show ipv6 route
ping ipv6 ipv6_address

## Slide 46: Next hop static ipv6 routes

## Slide 47: Directly connected ipv6 static route

## Slide 48: Fully specified ipv6 static route

## Slide 49: Default static ipv6 route
R(config)# Ipv6 route ::/0 {ipv6-address | exit-intf}

## Slide 50: Default static ipv6 route

## Slide 51: Configure a floating static route

## Slide 52: Test a floating static route
When R2 serial interfaces are shutdown.

## Slide 53: Troubleshooting
ping
traceroute
show ip route
show ip interface brief
show cdp neighbors detail

## Slide 54: Summary
Router functionality
Routing decisions and operation
  Switching packets between networks
  Path determination
  The routing table
Types of routes
Static routes
  IPv4 and IPv6
  Directly connected, default, floating
  Configuration
Troubleshooting

## Slide 55: Activities and labs
15.6.1– Packet Tracer - Configure IPv4 and IPv6 static and default routes